## Slide 1: Memory Management Units for Instruction and Data Cache for OR1200 CPU Core
Arijit Banerjee ASIC/SOC Class 2014
Dated 05/09/2014

## Slide 2: Motivation
ASICs/SoCs have billions of transistors
  Impossible to design everything manually
Cad tools to the rescue
To learn the basic full cad flow for ASIC/SoC design
MMU hard IP design as part of full processor design project

## Slide 3: Overview of Memory Management Unit
Memory Management Unit (MMU) an essential module in modern processors
Manages translation of virtual (logical) memory address space to physical address space
Provides memory protection for software programs
Source : http://en.wikipedia.org/wiki/File:MMU_principle_updated.png

## Slide 4: Introduction to OR1200 and Its MMUs
Two MMUs defined
Instruction MMU
  Controls I cache
Data MMU
  Controls D cache
Interfacing with wishbone bus interface
Source: OR1200 Specification

## Slide 5: MMU Address translation Mechanism in OR1200 MMUs
MMU divides the virtual address space into pages
It uses an in-memory table of items called “page table” that contains a “page table entry” (PTE) per page, to map the virtual page numbers to physical memory
PTE has an associative cache called translation lookaside buffer (TLB) to avoid accessing main memory per address translation
Source: OR1200 Specification

## Slide 6: Basic Cad Flow for MMU Hard IP Design
Source HDL Modification
Synthesis of individual blocks
Formal Verification
Place and Route

## Slide 7: Simulation
Tool used
  Synopsys VCS
Issues
  Functionality of the MMU was not documented explicitly
  Hard to interpret functionality using the lengthy modular Verilog code
  Simulated using random inputs

## Slide 8: Design Synthesis
Tool Used
  Design Compiler
Synthesized IMMU and DMMU separately
Clock and Reset pins had slow timing constraints of 50ns
Default Input/output pin-load constraints
Actual SRAM memory Verilog was integrated as black box for synthesis

## Slide 9: Synthesis Result Snaps
IMMU Synthesis snapshot

## Slide 10: Formal Verification
Tool used
  Formality
SRAMs were treated as black boxes in the verification
SRAM Verilog was ports only for comparison
Successfully verified both IMMU and DMMU

## Slide 11: Milkyway Database Preparation for SRAM Hard Macros
Created the Tutorial for SRAM hard macro data base preparation
Method
  Create the library and attach the technology file
  Import the DEF there after
Issues
  Directly DEF imports fails due as the DEF does not have technology file information
  Verilog and DEF has port mismatch due to SRAM compiler bug for Verilog generation

## Slide 12: Place and Route
Tools use
  IC Compiler (ICC)
Used the SRAM hard macro Milkyway databases
  64X14, 64X22 and 64x24 macros
IMMU need manual floor planning as SRAM macros were overlapping on top of each other
  Placement of Hard macros were fixed
  Placement blockage was placed over the SRAM macros
DMMU uses normal scripted flow

## Slide 13: ICC Result Snapshots
Before fixing the aspect ratio DMMU and IMMU
246 X246 square microns

## Slide 14: ICC Result Snapshots
After fixing the aspect ratio at 1.318 for DMMU and IMMU
289X220 square microns

## Slide 15: Deliverables
Wiki updated with all the deliverable materials including the Milkyway database creation with SRAM DEFs tutorial
Scripts uploaded in wiki
  DVE
  DC
  Formality
  ICC
SRAM Milkyway databases for macros 64x14, 64x22 and 64x24 uploaded in wiki and collab
Full placed and routed macro uploaded in collab dropbox

## Slide 16: Issues Faced
Had less time to learn the full flow
  Skipped the Hercules DRC and LVS for the design
  Also skipped Primetime signoff
Place and route using ICC showed following issues those are yet to be resolved
  Floating net issues flags errors
  VDD and VSS disconnection errors
  In some cases, for unknown causes the ICC takes infinitely long time to check “Notch DRCs”

## Slide 17: Conclusion
We learned a great deal of information about the full cad flow for ASIC/SoC design
Also learned about the OR1200 and its DMMUs and in general MMU’s internal working mechanism
Had hands on tools and its flows like VCS, DC, Formality, ICC etc.
Delivered the final Milkyway database for the DMMU and IMMU within the course time
However, had issues with ICC about net connection errors those are yet to debug

## Slide 18: Future Possibility
To start the project earlier after two to three weeks from starting
Collect more information about the ICC flow and Develop a concrete ICC flow that works
Include EMIR in the ICC flow (already made the tutorial )
Include Hercules DRC and LVS verification for the final layouts
Signoff timing checks using prime time
(Integrate a full project and tapeout)

## Slide 19: Questions

## Slide 20: Overview contd.
TLB is not mandatory; however it improves address translation speed
A PTE can include information about
  If the page is written
  When it was last used
  What process has the PTE associated with
  Weather or not it should be cached etc.